## Slide 1: Aviation System Block Upgrades Module N° B0-65/PIA-1 Optimization of Approach Procedures Including Vertical Guidance
Workshop on preparations for ANConf/12 − ASBU methodology
(Nairobi, 13-17 August 2012)
SIP/2012/ASBU/Nairobi-WP/16 A

## Slide 2: Module N° B0-65 Optimization of Approach Procedures Including Vertical Guidance
Summary | PBN-T: First step toward universal implementation of GNSS-based approaches. Achieved through application of Basic GNSS, Baro VNAV, SBAS and GLS.
Main Performance Impact | KPA-01 Access/Equity, KPA-02 Capacity, KPA-04 Efficiency, KPA-05 Environment, KPA-10 Safety
Operating Environment/Phases of Flight | Approach
Applicability Considerations | This module is applicable to all instrument and precision instrument runway ends, and to a limited extent, non-instrument runway ends
Global Concept Component(s) | AUO – Airspace User Operations AO – Aerodrome Operations
Global Plan Initiatives (GPI) | GPI-5 RNAV and RNP (PBN); GPI-14 Runway Operations GPI-20 WGS84
Main dependencies | NIL

## Slide 3: Module N° B0-65 Optimization of Approach Procedures Including Vertical Guidance
Global readiness checklist |  | Status (ready now or estimated date).
 | Standards readiness |  (B0 - GLS CAT I only)
 | Avionics availability | 
 | Ground system availability | 
 | Procedures available | 
 | Operations approvals | 

## Slide 4: Module N° B0-65 – Baseline
Limited number of GNSS-based PBN implemented, compared with conventional procedures.

## Slide 5: Module N° B0-65 – Change Brought by the Module
PBN-Terminal procedures require no ground-based Nav Aids .
Allows designers complete flexibility in determining final approach lateral /vertical paths.
States can implement GNSS-based PBN approach procedures with basic GNSS avionics with or without Baro VNAV capability, and for aircraft equipped with SBAS/GBAS avionics.
Designed for runways with or without conventional approaches  providing benefits to PBN-capable aircraft.
Key to maximum benefits is aircraft equipage.

## Slide 6: Module N° B0-65 – Intended Performance Operational Improvement
Access and Equity | Increased aerodrome accessibility
Capacity | Removal of requirement for sensitive and safety-critical areas resulting in increased runway capacity.
Efficiency | Benefits of lower approach minima: fewer diversions, over flights, cancellations and delays resulting in reduced fuel burn
Environment | Reduced CO2
Safety | Stabilized approach paths
CBA | Aircraft operators and ANSPs can quantify the benefits of lower minima by using historical aerodrome weather observations and modelling airport accessibility with existing and new minima. CBA is positive

## Slide 7: Module N° B0-65 – Necessary Procedures (Air & Ground)
Documents providing background and implementation guidance for ANS providers, aircraft operators, airport operators and aviation regulators:
  PBN Manual
  GNSS Manual
  Annex 10
  PANS-OPS Volume I
  Manual on Testing of Radio Navigation Aids (Doc 8071) Volume II
  Quality Assurance Manual for Flight Procedure Design (Doc 9906)

## Slide 8: Module N° B0-65 – Necessary System Capability
Avionics
  PBN approach procedures can be flown with basic IFR GNSS avionics
  Basic IFR GNSS receivers integrated with Baro VNAV functionality to support vertical guidance to LNAV/VNAV minima
  Aircraft with SBAS avionics can fly approaches with vertical guidance to LPV minima, as low as ILS Cat I minima
  Aircraft require GBAS avionics to fly GLS approaches
Ground Systems
  SBAS-based procedures do not require infrastructure at the airport, but SBAS elements (e.g. reference stations, master stations, GEO satellites) must be in place
  A GBAS station can support vertically guided Cat I approaches to all runways at that aerodrome

## Slide 9: Module N° B0-65 – Training and Qualification Requirements
Training in the operational standards and procedures are required for this module
Likewise, the qualifications requirements are identified in the regulatory requirements

## Slide 10: Module N° B0-65 – Regulatory/Standardization Needs and Approval Plan (Air &Ground)
Regulatory/Standardization:
  No new or updated regulatory guidance or standards documentation is needed at this time.
Approval Plans:
  No new or updated approval criteria is needed at this time. Implementation plans should reflect available aircraft, ground systems and operational approvals

## Slide 11: Module N° B0-65 – Reference Documents
Standards
  ICAO Annex 10 — Aeronautical Telecommunications, Volume I — Radio Navigation Aids. As of 2011 a draft SARPs amendment for GLS to support Category II/III approaches is completed and is being validated by States and industry.
Procedures
  ICAO Doc 8168, Aircraft Operations.
Guidance Material
  ICAO Doc 9674, World Geodetic System — 1984 (WGS-84) Manual;
  ICAO Doc 9613, Performance-based Navigation (PBN) Manual;
  ICAO Doc 9849, Global Navigation Satellite System (GNSS) Manual;
  ICAO Doc 9906, Quality Assurance Manual for Flight Procedure Design, Volume 5 — Validation of Instrument Flight Procedures;
  ICAO Doc 8071, Manual on Testing of Radio Navigation Aids, Volume II — Testing of Satellite-based Radio Navigation Systems;
  ICAO Doc 9931, Continuous Descent Operations (CDO) Manual.
Approval Documents
  FAA AC 20-138(), TSO-C129/145/146()
  ICAO Doc 4444, Procedures for Air Navigation Services — Air Traffic Management;
  ICAO Flight Plan Classification;
  ICAO Doc 8168, Aircraft Operations;
  ICAO Doc 9613, Performance Based Navigation Manual;
  ICAO Annex 10 — Aeronautical Telecommunications;
  ICAO Annex 11 — Air Traffic Services;
  ICAO Doc 9674, World Geodetic System — 1984 (WGS-84) Manual

## Slide 12: Module N° B0-65 Implementation - Benefits and Elements
Optimization of Approach Procedures Including Vertical Guidance
Elements
  APV with Baro VNAV
  APV with SBAS
  APV with GBAS
  To be reflected in ANRF
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | Y | Y | Y | Y | Y