## Slide 1: Aviation System Block Upgrades Module N° B0-75/PIA-1 Safety and Efficiency of Surface Operations (A-SMGCS Level 1-2)
Workshop on preparations for ANConf/12 − ASBU methodology
(Nairobi, 13-17 August 2012)
SIP/2012/ASBU/Nairobi-WP/16C

## Slide 2: Module N° B0-75 Safety and Efficiency of Surface Operations (A-SMGCS Level 1-2)
Summary | Basic A-SMGCS provides surveillance and alerting of movements of both aircraft and vehicles on the aerodrome thus improving runway/aerodrome safety. | 
Main Performance Impact | KPA-1 Access and Equity; KPA-02 Capacity; KPA-04 Efficiency; KPA-05 Environment; KPA-10 Safety | 
Domain / Flight Phases | Aerodrome surface movements (aircraft /vehicles), taxi, push-back, parking | 
Applicability Considerations | Any aerodrome/all classes of aircraft/vehicles. Implementation based on requirements from individual aerodrome operational and cost-benefit assessments. | 
Global Concept Component(s) | AO – Aerodrome Operations CM – Conflict Management | 
Global Plan Initiatives () | GPI-9 Situational Awareness GPI-13 Aerodrome Design and Management GPI-16 Decision Support Systems and Alerting Systems | 
Main Dependencies | - Non-cooperative aerodrome surveillance in form of surface movement radar (SMR), although SMR could be installed simultaneously with A-SMGCS. | 
Global Readiness Checklist |  | Status
 | Standards Readiness | ready
 | Avionics Availability | ready
 | Infrastructure Availability | ready
 | Ground Automation Availability | ready
 | Procedures Available | ready
 | Operations Approvals | ready

## Slide 3: Module N° B0-75 - Baseline
Historically, ANSP personnel and flight crew visually scan surface operations
  Both have as basis taxi management & as aircraft navigation/separation
Enhanced surface situational awareness based upon use of an aerodrome surface movement primary radar system and display (SMR).
Visual aids, Wild life strike hazard reduction
  (Not included in the Module but mapped to this Module)

## Slide 4: Module N° B0-75 – Change Brought by the Module
Element 1- Surveillance
  Enhances primary radar surface surveillance with the addition of at least one cooperative surface surveillance system.
  Systems include Multilateration, Secondary Surveillance Radar Mode S, Automatic Dependent Surveillance – Broadcast (ADS-B)
    Marginal improvement in routine management of taxi operations
    More efficient sequencing of aircraft departures.
Element 2 – Alerting
  Alerting with flight identification information improves the ATC response to situations requiring resolution ex: runway incursion incidents and improved response times to unsafe surface situations
  Levels of sophistication vary considerably

## Slide 5: Module N° B0-75 - Intended Performance Operational Improvement
Access and Equity | Improves access to portions of the manoeuvring area obscured from view of the control tower for vehicles and aircraft.
Capacity | Sustained levels of aerodrome capacity for visual conditions reduced to minima. ADS-B APT: potentially improve capacity for medium complexity aerodromes
Efficiency | Reduced taxi times and hence reduced fuel burn,
Environment | Reduced emissions
Safety | Reduced runway incursions.
CBA | A positive CBA can be made from improved efficiencies in surface operations leading to significant savings in aircraft fuel usage.

## Slide 6: Module N° B0-75 – Necessary Procedures (Air & and Ground)
Flight crew procedures specific to A-SMGCS are not beyond those associated with basic operation of aircraft transponder systems and settings of aircraft identification.
Vehicle drivers must be in a position to effectively operate vehicle transponder systems.
ATC is required to apply procedures specific to A-SMGCS

## Slide 7: Module N° B0-75 – Necessary System Capability
Avionics
  Existing aircraft ADS-B and/or SSR transponder systems, including correct setting of aircraft identification.
Vehicles
  Vehicle cooperative transponder systems, type as a function of the local A-SMGCS installation. Industry solutions readily available
Ground systems
  A-SMGCS: The surface movement radar should be complemented by a cooperative surveillance means allowing to track aircraft and ground vehicles. A surveillance display including some alerting functionalities is required in the tower.
  ADS B APT: cooperative surveillance infrastructure deployed on the aerodrome surface; installation of a tower traffic situational awareness display.

## Slide 8: Module N° B0-75 – Training and Qualification Requirements
    Training in the operational standards and procedures are required for this module
    Likewise, the qualifications requirements are identified in the regulatory requirements in Section 6 which form an integral part to the implementation of this module.

## Slide 9: Module N° B0-75 – Regulatory/Standardization needs and Approval Plan (Air & Ground)
Standards approved for aerodrome Multilateration, ADS-B and safety logic systems exist for use in:
  Europe
  The United States
  Other member States.
Standards for SMR exist for use globally

## Slide 10: Module N° B0-75 – Reference Documents
Standards
  Community Specification on A-SMGCS Levels 1 and 2;
  ICAO Doc 9924, Aeronautical Surveillance Manual;
  ICAO Doc 9871, Technical Provisions for Mode S Services and Extended Squitter;
  ICAO Doc 9830, Advanced Surface Movement Guidance and Control Systems (A-SMGCS) Manual;
  ICAO Doc 7030/5, (EUR/NAT) Regional Supplementary Procedures, Section 6.5.6 and 6.5.7;
  FAA Advisory Circulars:
  AC120-86 Aircraft Surveillance Systems and Applications
  AC120-28D Criteria for Approval of Category III Weather Minima for Take-off, Landing, and Rollout
  AC120-57A Surface Movement Guidance and Control System
  Avionics standards developed by RTCA SC-186/Eurocae WG-51 for ADS-B
  Aerodrome map standards developed by RTCA SC-217/Eurocae WG-44
  EUROCAE ED 163 Safety, Performance and Interoperability Requirements document for ADS B Airport Surface surveillance application (ADS-B APT)
ATC Procedures
  ICAO Doc 4444, Procedures for Air Navigation Services — Air Traffic Management; and
  ICAO Doc 7030, Regional Supplementary Procedures (EUR SUPPS).
Guidance material
  FAA NextGen Implementation Plan
  European ATM Master Plan

## Slide 11: Module N° B0-75 Implementation - Benefits and Elements
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | Y | Y | Y | Y | Y
Safety and Efficiency of Surface Operations (A-SMGCS Level 1-2)
Elements: 1. Visual aids, Wild life strike hazard reduction
  (Not included in the Module)
  2. Multilateration, SSR Mode S, and ADS-B;
  3. Transponder for both aircraft and vehicles
  3. Alerting systems with flight identification information
  To be reflected in ANRF