## Slide 1: Aviation System Block Upgrades Module N° B0-10/PIA 3 Improved Operations through Enhanced En-Route Trajectories
SIP/2012/ASBU/Nairobi-WP/24 A
Workshop on preparations for ANConf/12 − ASBU methodology
(Nairobi, 13-17 August 2012)

## Slide 2: Module N° B0-10 Improved Operations through Enhanced En-Route Trajectories
Summary | To allow the use of airspace which would otherwise be segregated (i.e. military airspace) along with flexible routing (Enroute-PBN) adjusted for specific traffic patterns. | 
Main Performance Impact | -KPA01 Access & Equity -KPA02 Capacity -KPA04 Efficiency -KPA05 Environment -KPA06 Flexibility -KPA09 Predictability | 
Operating Environment/Phases of Flight | En-route, TMA | 
Applicability Considerations | en-route airspace.The larger the size of the concerned airspace the greater the benefits, in particular for flextrack aspects. Benefits accrue to individual flights and flows. Application will naturally span over a long period as traffic develops. Its features can be introduced starting with the simplest ones. | 
Global Concept Component(s) | AOM – Airspace Organisation & Management AUO– Airspace Users Operations DCB – Demand-Capacity Balancing | 
Global Plan Initiatives | GPI-1 Flexible use of airspace GPI-4 Align upper airspace classifications GPI-7 Dynamic and Flexible Management GPI-8 Collaborative airspace design and management | 
Global Readiness Checklist |  | Status
 | Standards Readiness | Ready
 | Avionics Availability | Ready
 | Ground Systems Availability | Ready
 | Procedures Available | Ready
 | Ready | Ready

## Slide 3: Module N° B0-10 - Baseline
Varies from States and regions
  Fixed route network
  limited use of RNAV
  Rigid allocation of airspace between civil and military authorities

## Slide 4: Module N° B0-10 – Change Brought by the Module
Element 1  Airspace Planning
  Activities to organise and manage airspace prior to the time of flight
  Includes CDM applications for En-Route Airspace
Element 2  FUA: Flexible Use of Airspace
  Airspace should not be designated as either purely civil or purely military airspace, but should be considered as one continuum in which all users’ requirements are accommodated to the maximum extent possible.
Element 3  Flexible Routing (Enroute-PBN)
  Design of routes (or tracks) to match the traffic pattern and other variable factors such as weather- RNP 2/ Advance RNP
  When already in place, flex tracks systems can be improved in line with the new capabilities of ATM and aircraft, such as PBN and ADS.
  A current application of the element is DARPS, Dynamic Air route Planning System, used in the Pacific Region

## Slide 5: Module N° B0-10 – Intended Performance Operational Improvement
Access and Equity | Better access to airspace by a reduction of the permanently segregated volumes.
Capacity | The FUA gives greater possibilities to separate flights horizontally. PBN helps to reduce route spacing and aircraft separations. This in turn allows reducing controller workload by flight.
Efficiency | In particular the module will reduce flight length and related fuel burn. The potential savings are a significant proportion of the ATM related inefficiencies. The module will reduce the number of flight diversions and cancellations.
Environment | Emissions will be reduced
Flexibility | The various tactical functions allow to react rapidly to changing conditions.
Predictability | Improved planning allows stakeholders to anticipate on expected situations and be better prepared.
CBA | The ground costs are lower than the benefits to airspace users.

## Slide 6: Module N° B0-10 – Necessary Procedures (Air & Ground)
Element 1  Airspace Planning
  Required procedures exist for the main. They may need to be complemented by local practical guidance and processes
  The airspace requirements (RNAV, RNP and the value of the performance required) may require new ATS procedures and ground system functionalities
Element 2  FUA: Flexible Use of Airspace
  The ICAO Circular 330 AN/189 Civil/Military Cooperation in Air Traffic Management offers guidance and examples of successful practices of Civil and Military Cooperation
Element 3  Flexible Routing (enroute PBN)
  A number of operational issues and requirements will need to be addressed to enable harmonized deployment of Flex Route operations in a given area such as:
    Some adaptation of Letters of Agreement;
    Revised procedures to consider the possibility of transfer of control at other than published fixes;
    Review of controller manuals and current operating practices
    Specific communication and navigation requirements

## Slide 7: Module N° B0-10 – Necessary System Capability
Avionics
  FANS 1/A
Ground Systems
  CDM can be supported by a form of internet portal.
  Basic FUA concept can be implemented with the existing technology. For more advanced use of conditional routes, a robust collaborative decision system is required.
  ANSPs evaluate their FDPS to determine what, if any, modifications will be required to accommodate the implementation of Flex Route operations

## Slide 8: Module N° B0-10 – Training and Qualification Requirements
The required training is available and the change step is achievable from a human factors perspective. Training in the operational standards and procedures are required for this Module.
Likewise, the qualifications requirements are identified in the regulatory requirements

## Slide 9: Module N° B0-10 – Regulatory /Standardization needs and Approval Plan (Air & Ground)
Element 1  Airspace Planning
  ICAO material is available
Element 2  FUA: Flexible Use of Airspace
  ICAO provisions related to coordination between civil and military in support to the Flexile Use of Airspace can be found in several Annexes, PANS and Manuals
Element 3  Flexible Routing
  LoA/LoCs: Letters of agreement (LoA) and/or letters of coordination (LoC) might be required to reflect the specificities of Flex Route operations. Local hand-off procedures, timings and frequency allocations must be clearly detailed
Approval Plans: To Be Determined, based upon regional applications. Possible regional mandates of PBN should be considered.

## Slide 10: Module N° B0-10 – Reference Documents
Standards
  ICAO Doc 4444, Procedures for Air Navigation Services — Air Traffic Management, Chapter 5
Procedures: Nil
Guidance Material
  ICAO Doc 9426, Air Traffic Services Planning Manual;
  ICAO Doc 9554, Manual Concerning Safety Measures Relating to Military Activities Potentially Hazardous to Civil Aircraft Operations;
  ICAO Doc 9613, Performance-based Navigation (PBN) Manual;
  ICAO Doc 9689, Manual on Airspace Planning Methodology for the Determination of Separation Minima;
  ICAO Global Collaborative Decision Making (CDM) Guidelines (under development);
  ICAO Circular 330 AN/189, Civil/Military Cooperation in Air Traffic Management.
Approval Documents
  ICAO Doc 9426, Air Traffic Services Planning Manual;
  ICAO Doc 9689, Manual on Airspace Planning Methodology for the Determination of Separation Minima;
  ICAO Doc 9613, Performance-based Navigation (PBN) Manual;
  ICAO Doc 9554, Manual Concerning Safety Measures Relating to Military Activities Potentially Hazardous to Civil Aircraft Operations;
  ICAO Global Collaborative Decision Making (CDM) Guidelines (under development)
  ICAO Circular 330 AN/189 Civil/Military Cooperation in Air Traffic Management

## Slide 11: Module N° B0-10 Implementation - Benefits and Elements
Improved Operations through Enhanced En-Route Trajectories
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | Y | Y | Y | Y | N
Elements:
  1. Airspace planning and application of CDM
  2. Flexible Use of Airspace
  3. Flexible Routing –Enroute PBN
  To be reflected in ANRF