## Slide 1: Aviation System Block Upgrades Module N° B0-20/PIA-4 Improved Flexibility and Efficiency in Departure Profiles
SIP/2012/ASBU/Nairobi-WP/28C
Workshop on preparations for ANConf/12 − ASBU methodology
(Nairobi, 13-17 August 2012)

## Slide 2: Module N° B0-20 Improved Flexibility and Efficiency in Departure Profiles
Summary | To implement Continuous Climb Operations in conjunction with PBN | 
Main Performance Impact | KPA-04 – Efficiency; KPA-05 – Environment; KPA-10 - Safety | 
Operating Environment/Phases of Flight | Departure and En-Route | 
Global Concept Component(s) | AUO – Airspace user operations TS – Traffic synchronization AOM – Airspace organization and management | 
Global Plan Initiatives (GPI) | GPI 5- RNAV/RNP (Performance. Based Navigation) GPI-10- Terminal Area Design and Management GPI-11- RNP and RNAV SIDs and STARs | 
Pre-Requisites | NIL | 
 |  | Status
Global Readiness Checklist | Standards Readiness | Ready
 | Avionics Availability | Ready
 | Infrastructure Availability | Ready
 | Ground Automation Availability | Ready
 | Procedures Available | Ready
 | Operations Approvals | Ready

## Slide 3: Module N° B0-20 - Baseline
Varies from one State/region to the next.
Some aspects of the movement to PBN have already been subject of local improvements in areas

## Slide 4: Module N° B0-20 – Change Brought by the Module
Continuous Climb Operations
  CCO is an aircraft operating technique aided by appropriate airspace and procedure design and appropriate ATC clearances
  A CCO can be flown with or without the support of function of the FMS
Performance -based Navigation (PBN)
  The PBN concept encompasses two types of navigation specifications RNAV/RNP:
  PBN SIDs

## Slide 5: Module N° B0-20 – – Intended Performance Operational Improvement
Efficiency | Reduced fuel burn and efficient aircraft operating profiles.; Reduction in the number of required radio transmissions. | 
Environment | Authorization of operations where noise limitations would otherwise result in operations being curtailed or restricted. Environmental benefits through reduced emissions. | 
Safety | More consistent flight paths. Lower pilot and Air Traffic Control workload. | 
CBA | CCO benefits are heavily dependent on each specific ATM environment. If implemented within the ICAO CCO manual framework, the benefit/cost ratio (BCR) will be positive. | 

## Slide 6: Module N° B0-20 – Necessary Procedures (Air & Ground)
The ICAO Performance-based Navigation Manual (Doc 9613)-Provides general guidance on PBN implementation
The Continuous Climb Operations (CCO) Manual (Doc xxxx); Provides guidance on
    Airspace design
    Instrument flight procedures
    ATC facilitation
    Flight techniques necessary to enable CC0s

## Slide 7: Module N° B0-20 – Necessary System Capabilities
Avionics
  CCO does not require specific air/ground technology.
  CCO is an aircraft operating technique aided by appropriate airspace and procedure design, and appropriate ATC clearances
Ground systems
  Controllers would benefit from some automation support to display aircraft capabilities in order to know which aircraft can do what

## Slide 8: Module N° B0-20 – Training and Qualification Requirements
    Training in the operational standards and procedures are required for this module
    Likewise, the qualifications requirements are identified in the regulatory requirements

## Slide 9: Module N° B0-20 – Regulatory/standardization needs and Approval Plan (Air and Ground)
Regulatory/Standardization
  Use current published requirements
Approval Plans
  Must be in accordance with application requirements

## Slide 10: Module N° B0-20 – Reference Documents
Procedures
  ICAO Doc 8168, Procedures for Air Navigation Services- Aircraft Operations
  ICAO Doc 4444, Procedures for Air Navigation Services — Air Traffic Management.
  ICAO Doc 9613, Performance-based Navigation (PBN) Manual;
  ICAO Doc xxxx, Continuous Climb Operations (CCO) Manual
Approval Documents
  ICAO Doc XXXX, Continuous Climb Operations Manual;
  ICAO Doc 9613, Performance Based Navigation Manual;
  ICAO Doc 4444, Procedures for Air Navigation Services — Air Traffic Management.

## Slide 11: Module N° B0-20 Implementation - Benefits and Elements
Improved Flexibility and Efficiency in Departure Profiles
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | N | N | Y | Y | Y
  Elements: CCO and PBN SIDs
  No avionics or Ground systems required
  To be reflected in ANRF