## Slide 1: Aviation System Block Upgrades Module N° B0-70/PIA-1 Increased Runway Throughput through Wake Turbulence Separation
SIP/2012/ASBU/Dakar-WP/16 B
Workshop on preparations for ANConf/12 − ASBU methodology
(Dakar, 16-20 July 2012)

## Slide 2: Module N° B0-70 Increased Runway Throughput through Wake Turbulence Separation
Summary | Improved throughput on departure & arrival runways through revision of current ICAO wake turbulence separation minima and procedures. | 
Main Performance Impact | KPA-02 – Capacity, KPA-06 Flexibility | 
Domain / Flight Phases | Arrival and Departure | 
Applicability Considerations | Implementation of re-categorized wake turbulence is procedural. No changes to automation systems. | 
Global Concept Component(s) | CM – Conflict Management | 
Global Plan Initiatives () | GPI-13- Aerodrome Design; GPI 14 – Runway Operations | 
Main Dependencies | Nil | 
Global Readiness Checklist |  | Status
 | Standards Readiness | 2013
 | Avionics Availability | N/A
 | Ground Systems Availability | N/A
 | Procedures Available | 2013
 | Operations Approvals | 2013

## Slide 3: Module N° B0-70 - Baseline
ANSP applied wake mitigation procedures since 1990s
1990s standards are conservative in terms of required
aircraft-to-aircraft wake separations:

## Slide 4: Module N° B0-70 – Change Brought by the Module
Changes to ANSPs applied wake mitigation procedures
Element 1  Revision of current ICAO wake separation minima
  20 year old wake separation standards still provide safe separation of aircraft
  No longer provides capacity efficient spacing and sequencing of aircraft in approach and en-route operations
Element 2  Increasing Aerodrome Arrival Operational Capacity
  Prior to 2008, instrument landing operations conducted to an aerodrome’s CSPR needed the wake separation spacing equivalent to conducting instrument landing operations to a single runway
  Variations of the procedure are being developed allowing its application to more aerodrome CSPR with fewer constraints
Element 3  Increasing Aerodrome Departure Operational Capacity
  Wake Independent Departure and Arrival Operation (WIDAO) developed by France and Wake Turbulence Mitigation for Departures (WTMD) project developed by US allows the ANSP to use the inner CSPR for departures independent of the arrivals on the outer CSPR

## Slide 5: Module N° B0-70 – Intended Performance Operational Improvement
Capacity | Aerodrome capacity & departure/arrival rates raise as wake categories are increased from 3 to 6. New procedures will modify current wake mitigation measures of waiting for 2-3 minutes & decrease waiting time required. Aerodrome capacity & departure rates will increase. Runway occupancy time will decrease.
Flexibility | ANSP chose to configure aerodromes to operate on 3 or 6 categories
CBA | Benefits the users of the aerodrome’s runways. Air carrier data shows when operating from a major hub operation at a U.S. aerodrome, a gain of two extra departures/hr from the aerodrome’s CSPR during the “rush” has a major beneficial effect in reducing delays in the air carrier’s operations.

## Slide 6: Module N° B0-70 – Necessary Procedures (Air & Ground)
ANSP will need automation support in providing the wake category assignment of aircrafts to controllers.
Implementing Element 1:
  no changes to air crew’s procedures.
  Impact on use of aerodromes CSPR for arrivals will affect the ANSP procedures for sequencing and segregating aircraft to the CSPR.
Implementing Element 2 :
  no changes to aircrew’s procedures.
  affects the ANSP procedures for sequencing and segregating aircraft to the CSPR
Implementing Element 3:
  no changes to the aircrew’s procedures
  affects the ANSP procedures for departing aircraft on an aerodrome’s CSPR & for accomplishing a departure from the aerodrome.

## Slide 7: Module N° B0-70 – Necessary System Capability
Avionics
  No additional technology for the aircraft or additional aircrew certifications is required.
Ground systems
  Some ANSPs may develop a support tool to aid in the application of the new set of 6 category ICAO wake separates.
  Element 2 and 3 products vary on their dependency to newly applied technology.
  For WTMD implementation requires wind sensors and automation support to predict crosswind strength and direction and to display that information to the ATC

## Slide 8: Module N° B0-70 – Training and Qualification Requirements
    Controllers will require training on additional wake categories and separation matrix. The addition of Element 3, WTMD, will require training for controllers on the use of the new tools to monitor and predict cross-winds.
    Likewise, the qualifications requirements are identified in the regulatory requirements

## Slide 9: Module N° B0-70 – Regulatory/Standardization Needs and Approval Plan (Air & Ground)
Regulatory/Standardization:
  Updates required to current published criteria
Approval Plans:
  To Be Determined following updates to standards. Note: Existing interim activities including those associated with FAA Wake Turbulence Mitigation for Departures (WTMD), and Wake Independent Departure and Arrival Operation (WIDAO) criteria in use at CDG will continue and are expected to be included in the ICAO revised material.

## Slide 10: Module N° B0-70 – Reference Documents
  Standards
  Procedures
  Guidance Materials
  Approval Documents
    ICAO Doc 4444, Procedures for Air Navigation Services — Air Traffic Management;
    ICAO Doc 9426, Air Traffic Services Planning Manual;
    FAA Order 7110.308.

## Slide 11: Module N° B0-70 Implementation - Benefits and Elements
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | N | Y | N | N | N
Increased Runway Throughput through Wake Turbulence Separation
Elements:
  1. Revision of current ICAO wake separation minima
  2. Increasing Aerodrome Arrival Operational Capacity
  3. Increasing Aerodrome Departure Operational Capacity
  To be reflected in ANRF