## Slide 1: Aviation System Block Upgrades Module N° B0-15/PIA 1 Improve Traffic Flow Through Runway Sequencing (AMAN/DMAN)
SIP/2012/ASBU/Dakar-WP/16E
Workshop on preparations for ANConf/12 − ASBU methodology
(Dakar, 16-20 July 2012)

## Slide 2: Module N° B0-15 Improve Traffic Flow Through Runway Sequencing (AMAN/DMAN)
Summary | To manage arrivals and departures to and from a multi-runway aerodrome or locations with multiple dependent runways at closely proximate aerodromes to efficiently utilize the inherent runway capacity | 
Main Performance Impact | KPA-02 Capacity - KPA-04 Efficiency KPA-09 Predictability - KPA-06 Flexibility | 
Applicability Considerations | Runways and Terminal Manoeuvring Area in major hubs and metropolitan areas will be most in need of these improvements. Runway Sequencing procedures are widely used in aerodromes globally. However, some locations might have to confront environmental and operational challenges | 
Global Concept Element(s) | TS – Traffic Synchronization | 
Global Plan Initiative | GPI-6 Air Traffic Flow Management | 
Global Readiness Checklist |  | Status
 | Standards Readiness | Ready
 | Avionics Availability | Ready
 | Ground System Availability | Ready
 | Procedures Available | Ready
 | Operations Approvals | Ready

## Slide 3: Module N° B0-15 - Baseline
Manual process by which the air traffic controller uses local procedures and his expertise to sequence departures or arrivals in real time.

## Slide 4: Module N° B0-15 – Change Brought by the Module
Element 1  AMAN
  Arrival management (AMAN)sequences the aircraft, based on the airspace state, wake turbulence, aircraft capability, and user preference. The smoothed sequence allows increase aerodrome throughput. Arriving flights are “metered” by Control Time of Arrival (CTAs) and must arrive at a defined point close to the aerodrome by this time.
Element 2  DMAN
  Departure management serves to optimize departure operations to ensure the most efficient utilization of aerodrome resources.
  Slots assignment and adjustments will be supported by departure management automations. Departure management sequences the aircraft, based on the airspace state, wake turbulence, aircraft capability, and user preference, to fit into the overhead

## Slide 5: Module N° B0-15 – – Intended Performance Operational Improvement
Capacity | Optimizes usage of terminal airspace and runway capacity Optimize utilization of terminal and runway resources
Efficiency | Harmonized arriving traffic flow from en-route to terminal and aerodrome through sequencing arrival flights; Iincreased runway throughput and arrival rates. Streamline departure traffic flow and decreased lead time for departure request. Automated dissemination of departure information and clearances.
Predictability | Decrease uncertainties in aerodrome/terminal demand prediction
Flexibility | Enables dynamic scheduling.
CBA | Business case built for Time Based Flow Management in US. Case proves that benefit/cost ratio is positive

## Slide 6: Module N° B0-15 – Necessary Procedures (Air & Ground)
The US TBFM and EUROCONTROL AMAN/DMAN efforts provide the systems and operational procedures necessary.
In particular, procedures for the extension of metering into en-route airspace will be necessary.
PBN for arrival will also be crucial as well.

## Slide 7: Module N° B0-15 – Necessary System Capability
Avionics
  No avionics capability is required
Ground Systems
  Automation support is needed for the synchronization of arrival sequencing, departure sequencing, and surface information;
  For AMAN/DMAN application, existing technologies can be leveraged, but require site adaptation and maintenance.

## Slide 8: Module N° B0-15 – Training and Qualification Requirements
Automation support is needed for Air Traffic Management in airspace with high demands. Thus, training is needed for ATM personnel.
Training in the operational standards and procedures are required
    Likewise, the qualifications requirements are identified in the regulatory requirements in Section 6 which form an integral part to the implementation of this module..

## Slide 9: Module N° B0-15 – Regulatory/Standardization Needs and Approval Plan (Air & Ground)
Regulatory/Standardization: Updates required to current published criteria
Approval Plans: To Be Determined.

## Slide 10: Module N° B0-15 – Reference Documents
Standards - NIL
Procedures -NIL
Guidance Materials
  European ATM Master Plan, Edition 1.0, March 2009, update in progress;
  SESAR Definition Phase Deliverable 2 – The Performance Target, December 2006;
  SESAR Definition Phase Deliverable 3 – The ATM Target Concept, September 2007;
  SESAR Definition Phase Deliverable 5 – SESAR Master Plan, April 2008;
  TBFM Business Case Analysis Report;
  NextGen Midterm Concept of Operations v.2.0;
  RTCA Trajectory Operations Concept of Use.
Approval Documents

## Slide 11: Module N° B0-15 Implementation - Benefits and Elements
Improve Traffic Flow Through Runway Sequencing (AMAN/DMAN)
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | N | Y | Y | N | N
Elements:
  1. AMAN
  2. DMAN
  To be reflected in ANRF