## Slide 1: Aviation System Block Upgrades Module N° B0-25/PIA-2 Increased Interoperability, Efficiency and Capacity through Ground-Ground Integration
Workshop on preparations for ANConf/12 − ASBU methodology
(Dakar, 16-20 July 2012)
SIP/2012/ASBU/Dakar-WP/21 A

## Slide 2: Module N° B0-25 Increased Interoperability, Efficiency and Capacity through Ground-Ground Integration
Summary | To improve coordination between ATS Units by using AIDC. | 
Main Performance Impact | KPA-02 Capacity - KPA-04 Efficiency KPA-07 Global Interoperability - KPA-10 Safety | 
Operating Environment/Phases of Flight | All flight phases and all type of ATS units | 
Applicability Considerations | Applicable to min. 2 ACCs dealing with en-route and/or TMA airspace. Greater number of consecutive participating ACCs  increase the benefits. | 
Global Concept Component(s) | CM - Conflict management IM - Information Management | 
Global Plan Initiatives (GPI) | GPI-16 Decision Support Systems | 
Pre-Requisites | Link with B0-40 | 
Global Readiness Checklist |  | Status
 | Standards Readiness | Ready
 | Avionics Availability | No requirement
 | Ground systems Availability | Ready
 | Procedures Available | Ready
 | Operations Approvals | Ready

## Slide 3: Module N° B0-25 - Baseline
Classical coordination by phone and procedural and/or radar distance separations
  Not included in this module but mapped to this module
    New Flight Plan 2012
    AMHS/IPS

## Slide 4: Module N° B0-25 – Change Brought by the Module
Implementation of the set of AIDC messages in the Flight Data Processing System (FDPS) of the different ATS units

## Slide 5: Module N° B0-25 – Intended performance Operational Improvement
Capacity | Reduced controller workload Increased data integrity supporting Reduced separations translating directly to cross sector or boundary capacity flow increases.
Efficiency | - Reduced separation can be offered more frequently to aircraft flight levels closer to the flight optimum; in certain cases, this also translates in reduced en-route holding.
Global Interoperability | Seamlessness: the use of standardised interfaces reduces the cost of development, allows controller to apply the same procedures at the boundaries of all participating centres and border crossing becomes more transparent to flights.
Safety | Better knowledge of more accurate flight plan information
CBA | Increase of throughput at ATC unit boundary, reduced ATCO Workload will exceed FDPS software changes cost.

## Slide 6: Module N° B0-25 – Necessary Procedures (Air & Ground)
Required procedures exist
Experience from other regions can be a useful reference

## Slide 7: Module N° B0-25 – Necessary System Capability
Avionics
  No specific airborne requirements
Ground Systems
  A set of AIDC messages in Flight Data Processing and could use the ground network standard AFTN-AMHS or ATN.
  Europe is presently implementing IP Wide Area Networks
  It also includes for oceanic ATSUs a function supporting transfer of communication via data link.

## Slide 8: Module N° B0-25 – Training and Qualification Requirements
Training for the automation support will be required.
Training in the operational standards and procedures are also required.
    Likewise, the qualifications requirements are identified in the regulatory requirements in Section 6 which form an integral part to the implementation of this module.

## Slide 9: Module N° B0-25 – Regulatory/Standardization needs and Approval Plan (Air & Ground)
Regulatory/Standardization: Use current published criteria that include:
  ICAO Doc 4444, Procedures for Air Navigation Services — Air Traffic Management;
  EU Regulation, EC No 552/2004.
Approval Plans: To Be Determined, based upon regional consideration of AIDC.

## Slide 10: Module N° B0-25 – Reference Documents
Standards
• ICAO Doc 4444, Procedures for Air Navigation Services - Air Traffic Management, Appendix 6 - ATS Interfacility Data Communications (AIDC) Messages
• ICAO Doc 9880, Manual on Detailed Technical Specifications for the Aeronautical Telecommunication Network (ATN) using ISO/OSI Standards and Protocols, Part II — Ground-Ground Applications — Air Traffic Services Message Handling Services (ATSMHS).
Procedures: To be determined.
Guidance Material
• ICAO Doc 9694, Manual of Air Traffic Services Data Link Applications; part 6
• GOLD Global Operational Data Link Document (APANPIRG, NAT SPG), June 2010;
• Pan Regional Interface Control Document for Oceanic ATS Interfacility Data Communications (PAN ICD) Coordination Draft Version 0.3. 31 August 2010;
• Asia/Pacific Regional Interface Control Document (ICD) For ATS Interfacility Data Communications (AIDC). ICAO Asia/Pacific Regional Office. http://www.bangkok.icao.int/edocs/icd_aidc_ver3.pdf
• EUROCONTROL Standard for On-Line Data Interchange (OLDI); and EUROCONTROL Standard for ATS Data Exchange Presentation (ADEXP)

## Slide 11: Module N° B0-25 Implementation - Benefits and Elements
Increased Interoperability, Efficiency and Capacity through Ground-Ground Integration
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | N | Y | Y | N | Y
Elements:
  - New Flight Plan (Not included in the Module)
  - AMHS/IPS (Not included in the Module)
  - AIDC
  To be reflected in ANRF