## Slide 1: Aviation System Block Upgrades Module N° B0-30/PIA-2 Service Improvement through Digital Aeronautical Information Management
SIP/2012/ASBU/Dakar-WP/21B
Workshop on preparations for ANConf/12 − ASBU methodology
(Dakar, 16-20 July 2012)

## Slide 2: Module N° B0-30 Service Improvement through Digital Aeronautical Information Management
Summary | Product centric to data centric. The initial introduction of digital processing and management of information, through AIS/AIM implementation, use of AIXM, migration to electronic AIP and better quality and availability of data. | 
Main Performance Impact | KPA-03 Cost-Effectiveness, KPA-05 Environment, KPA-07 Global Interoperability; KPA-10 Safety | 
Operating Environment/Phases of Flight | All phases of flight | 
Applicability Considerations | Applicable at State level, with increased benefits as more States participate | 
Global Concept Component(s) | IM – Information Management | 
Global Plan Initiatives () | -18 Electronic information services | 
Global Readiness Checklist |  | Status
 | Standards Readiness | Ready
 | Avionics Availability | Ready
 | Ground Systems Availability | Ready
 | Procedures Available | Ready
 | Operations Approvals | Ready

## Slide 3: Module N° B0-30 - Baseline
Current aeronautical Information service and processes
  Based on paper publications and text based NOTAMs
Not included in this Module but mapped to this Module
  WGS-84;
  eTOD; and
  QMS for AIM

## Slide 4: Module N° B0-30 – Change Brought by the Module
AIS moves into AIM
  AIXM /Standardised formats based on widely used information technology standards (UML, XML/GML).
  eAIP /The AIP moves from paper to electronic support.
  Digital NOTAM

## Slide 5: Module N° B0-30 – Intended Performance Operational Improvement
Cost Effectiveness | Reduced costs in terms of data inputs and checks, paper and post, especially when considering the overall data chain, from originators, through AIS, to the end users.
Environment | Reduced use of paper; also, more dynamic information should allow shorter flight trajectories, based on more accurate information about the current status of the airspace structure.
Global Interoperability | Essential contribution to interoperability
Safety | Reduction in the number of possible inconsistencies, as the module will allow to reduce the number of manual entries and ensure consistency among data through automatic data checking based on commonly agreed business rules.
CBA | The business case for AIXM has been conducted in and in the and has shown to be positive. The transition from paper products to digital data is a critical pre-requisite for the implementation of any current or future ATM or air navigation concept that relies on the accuracy, integrity and timeliness of the data.

## Slide 6: Module N° B0-30 – Necessary Procedures (Air &Ground)
ATC - No new procedures
Users - Full benefit requires new procedures for data users to retrieve the information digitally
  For example, for Airlines in order to enable the dynamic provision of the digital AIS data in the on-board devices, in particular Electronic Flight Bags

## Slide 7: Module N° B0-30 – Necessary System Capability
Avionics
  No avionics requirements.
Ground Systems
  AIS data made available to the AIS service through IT and to external users via either a subscription for an electronic access or physical delivery. Electronic access can be based on internet protocol services.
  The main automation functions that need to be implemented to support provision of electronic AIS are the national aeronautical data, NOTAM (both national and international) and meteorological management including data collection, verification and distribution.

## Slide 8: Module N° B0-30 – Training and Qualification Requirements
Training is required for AIS/AIM personnel.
Training in the operational standards and procedures are required for this module
Likewise, the qualifications requirements are identified in the regulatory requirements

## Slide 9: Module N° B0-30 – Regulatory/Standardization needs and Approval Plan ( Air &Ground)
Regulatory/Standardization: Use current published requirements
Approval Plans: To Be Determined, based upon regional applications.

## Slide 10: Module N° B0-30 – Reference Documents
Standards: TBD
Procedures :TBD
Guidance Material
  ICAO Doc 8126, Aeronautical Information Services Manual, incl. AIXM and eAIP
  ICAO Doc 8697, Aeronautical Chart Manual
  Manuals on AIM quality system and AIM training.

## Slide 11: Module N° B0-30 Implementation - Benefits and Elements
Service Improvement through Digital Aeronautical Information Management
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | N | N | N | Y | Y
Elements:
  - WGS-84; eTOD; and QMS for AIM (Not included in this Module)
  - AIXM
  - eAIP
  - Digital NOTAM
  to be reflected in ANRF