## Slide 1: Aviation System Block Upgrades Module N° B0-86/PIA-3 Improved Access to Optimum Flight Levels through Climb/Descent Procedures using ADS-B
SIP/2012/ASBU/Dakar-WP/24E
Workshop on preparations for ANConf/12 − ASBU methodology
(Dakar, 16-20 July 2012)

## Slide 2: Module N° B0-86 Improved Access to Optimum Flight Levels through Climb/Descent Procedures using ADS-B
Summary | This ITP module enables an aircraft to reach a more satisfactory flight level for flight efficiency or to avoid turbulence for safety. | 
Main Performance Impact | KPA-02 Capacity, KPA -04 Efficiency and KPA-05 Environment. | 
Operating Environment/Phases of Flight | En-Route | 
Applicability Considerations | This can be applied to routes in procedural airspaces, | 
Global Concept Component(s) | CM, AUO, AOM | 
Global Plan Initiatives (GPI) | GPI-9, GPI-7 | 
Pre-Requisites | NIL | 
Global Readiness Checklist |  | Status (ready now or estimated date).
 | Standards Readiness | √
 | Avionics Availability | √
 | Infrastructure Availability | √
 | Ground Automation Availability | √
 | Procedures Available | √
 | Operations Approvals | √

## Slide 3: Module N° B0-86 - Baseline
ITP using ADS-B is in operational use and hence can be considered to be a baseline.

## Slide 4: Module N° B0-86 – Change Brought by the Module
The introduction of ITP and ADS-B based separation minima enable aircraft to climb or descend through the altitude of other aircraft when the requirements for procedural separation cannot be met

## Slide 5: Module N° B0-86 – Intended Performance Operational Improvement
Capacity | Improvement in capacity on a given air route
Efficiency | Increased efficiency on oceanic and potentially continental en-route.
Environment | Reduced emissions
Safety | A reduction of possible injuries for cabin crew and passengers
CBA | To be determined

## Slide 6: Module N° B0-86 – Necessary Procedures (Air & Ground)
Procedures for ITP using ADS-B have been developed and a PANS-ATM Amendment is in progress.
Additional information will be available in an ICAO circular – “Safety Assessment for the development of Separation Minima and Procedures for In-Trail Procedure (ITP) using Automatic Dependant Surveillance – Broadcast (ADS-B) Version 1.5.4”
ITP requires the use of CPDLC as per PANS-ATM amendment for an applicability date of Nov 2013.

## Slide 7: Module N° B0-86 – Necessary System Capability
Avionics
  The aircraft performing the in-trail procedure will require an ADS-B IN capability compliant with DO-312/ED-159 or DO-317A/ED-194. The other aircraft involved in the procedure will require an ADS-B OUT capability compliant with AMC 20-24/DO-260A/DO-260B/ED-102A, or DO-317A/ED-194.
  CPDLC compliant with DO-306 chg 1 / ED-122 chg 1is required.
Ground Systems
  It is recommended that conflict probe logics be adapted to ITP separation minimum.

## Slide 8: Module N° B0-86 – Training and Qualification Requirements
The flight crew needs to be trained and qualified to understand the limitations of the equipment and to ensure a correct usage of the In-Trail Procedure and supporting avionics.
The controller needs to be trained and qualified to assume the tasks and to ensure a correct usage of the In-Trail Procedure and ground support tools.

## Slide 9: Module N° B0-86 – Regulatory/standardization needs and Approval Plan (Air and Ground)
Regulatory/Standardization
  Use current published criteria
Approval Plans
  To Be Determined.
  Operational Approval guidance/criteria may be needed based upon regional application for ATSA.

## Slide 10: Module N° B0-86 – Reference Documents
Standards
  EUROCONTROL ATSAW Deployment Plan(draft)
  EUROCAE ED-159 / RTCA DO-312 “Safety, Performance and Interoperability Requirements Document for the In-Trail Procedure in Oceanic Airspace (ATSA-ITP) Application”.
Procedures - TBD
Guidance Material: TBD
Approval Documents
  FAA AC 20-172a; and FAA TSO-C195a
  FAA Memo; Interim Policy and Guidance Automatic Dependent Surveillance Broadcast (ADS-B) Aircraft Surveillance Systems Supporting Oceanic In-Trail Procedures (ITP). Dated: May 10, 2010;
  DO-312/ED-159;
  DO-317A/ED-194;
  ICAO circular – “Safety Assessment for the development of Separation Minima and Procedures for In-Trail Procedure (ITP) using Automatic Dependant Surveillance – Broadcast (ADS-B) Version 1.5.4”.

## Slide 11: Module N° B0-86 Implementation - Benefits and Elements
Improved Access to Optimum Flight Levels through Climb/Descent Procedures using ADS-B
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | N | Y | Y | Y | Y
Elements:
  - ITP using ADS-B
  To be reflected in ANRF