## Slide 1: Aviation System Block Upgrades Module N° B0-05/ PIA 4 Improved Flexibility and Efficiency in Descent Profiles (CDOs)
SIP/2012/ASBU/Dakar-WP/28 A
Workshop on preparations for ANConf/12 − ASBU methodology
(Dakar, 4-6 July 2012)

## Slide 2: Module N° B0-05 Improved Flexibility and Efficiency in Descent Profiles (CDOs)
Summary | Deployment of performance-based airspace and arrival procedures that allow aircrafts to fly their optimum profile taking account airspace and traffic complexity with continuous descent operations (CDOs). | 
Main Performance Impact | KPA-03 – Cost-effectiveness; KPA-04 – Efficiency; KPA-09 - Predictability | 
Operating Environment/Phases of Flight | Approach/Arrivals and En-Route. | 
Global Concept Component(s) | AOM – Airspace Organisation and Management AO – Aerodrome Operations TS – Traffic Synchronisation, AOM | 
Global Plan Initiatives (GPI) | GPI-10- Terminal Area Design and Management; GPI-11- RNP and RNAV Standard instrument Departures (SIDS)and Standard Terminal Arrivals (STARS); | 
Pre-Requisites | NIL | 
Global Readiness Checklist |  | Status
 | Standards Readiness | Ready
 | Avionics Availability | Ready
 | Ground System Availability | Ready
 | Procedures Available | Ready
 | Operations Approvals | Ready

## Slide 3: Module N° B0-05 - Baseline
Varies from one State/region to the next.
Some aspects of the movement to PBN have already been subject of local improvements in areas

## Slide 4: Module N° B0-05 – Change brought by the Module
Element 1  Continuous Descent Operations (CDO)
  CDO is enabled by airspace design, procedure design and facilitation by ATC
  An optimum CDO starts from the top-of-descent (TOD) and uses descent profiles that reduce controller-pilot communications and segments of level flight.
Element 2  Performance -based Navigation (PBN)
  The PBN concept encompasses two types of navigation specifications RNAV/RNP:
  PBN STARs

## Slide 5: Module N° B0-05 – Intended Performance Operational Improvement
Efficiency | reduced fuel burn authorization of operations where noise limitations would otherwise result in operations being curtailed or restricted reduction in the number of required radio transmissions optimal management of the top-of-descent in the en-route airspace
Environment | Reduction on CO2 through reduced fuel burn
Safety | more consistent flight paths and stabilized approach paths reduction in the incidence of controlled flight into terrain (CFIT) reduction in the number of conflicts.
CBA | If implemented within the ICAO CDO manual framework, it is envisaged that the benefit/cost ratio (BCR) will be positive.

## Slide 6: Module N° B0-05 – Necessary Procedures (Air & Ground)
ICAO Continuous Descent Operations (CDO) Manual (Document 9931)
  Provides guidance on the airspace design, instrument flight procedures, ATC facilitation and flight techniques necessary to enable continuous descent profiles.
ICAO Performance-based Navigation Manual (ICAO Document 9613)
  Provides general guidance on PBN implementation.
ICAO PBN operational approval guidance material will be available by June 2012

## Slide 7: Module N° B0-05 – Necessary System Capability
Avionics
  CDO does not require specific air/ground technology.
  CDO is an aircraft operating technique aided by appropriate airspace and procedure design, and appropriate ATC clearances
Ground Systems
  RNP AR Approaches requires significant investment, ANSPs should work closely with airlines

## Slide 8: Module N° B0-05 – Training and Qualification Requirements
Training in the operational standards and procedures are required for this module
Likewise, the qualifications requirements are identified in the regulatory requirements

## Slide 9: Module N° B0-05 – Regulatory/standardization needs and Approval Plan (Air and Ground)
Regulatory/Standardization: Use current published requirements
Approval Plans: Must be in accordance with application requirements e.g. airspace design, air traffic operations, PBN requirements for fixed radius transitions, radius-to-fix legs, Required Time of Arrival (RTA), parallel offset, etc

## Slide 10: Module N° B0-05 – Reference Documents
Standards
  For flight plan requirements in Amendment 1, ICAO Document 4444; PANS/ATM v15
Procedures
Guidance Material
  ICAO Doc 9613, Performance-based Navigation (PBN) Manual; ICAO Doc 9931, Continuous Descent Operations (CDO) Manual;.
  FAA Advisory Circular, AC 90-105, Approval Guidance for RNP Operations and Barometric Vertical Navigation in the U.S. National Airspace System) which provides system and operational approval guidance for operators (only reflects the US situation).
Approval Documents
  ICAO Doc 9931, Continuous Descent Operations Manual;
  ICAO Doc 9613, Performance Based Navigation Manual;
  FAA AC120-108, CDFA.

## Slide 11: Module N° B0-05 Implementation - Benefits and Elements
Improved Flexibility and Efficiency in Descent Profiles (CDOs)
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | N | N | Y | Y | Y
  Elements: CDO and PBN STARs
  No avionics or Ground systems are required
  To be reflected in ANRF