## Slide 1: Aviation System Block Upgrades Module N° B0-40/PIA-4 Improved Safety and Efficiency through the initial application of Data Link En-Route
SIP/2012/ASBU/Dakar-WP/28B
Workshop on preparations for ANConf/12 − ASBU methodology
(Dakar, 16-20 July 2012)

## Slide 2: Module N° B0-40 Improved Safety and Efficiency through the initial application of Data Link En-Route
Summary | Implementation of an initial set of data link applications | 
Main Performance Impact | KPA-02 Capacity; KPA-04 Efficiency; KPA-10 Safety | 
Operating Environment/Phases of Flight | En-route flight phases, including areas where radar systems cannot be installed such as remote or oceanic airspace. | 
Applicability Considerations | Requires good synchronisation of airborne and ground deployment to generate significant benefits, in particular to those equipped. Benefits increase with the proportion of equipped aircraft. | 
Global Concept Component(s) | IM – Information Management SDM – Service Delivery Management | 
Global Plan Initiatives (GPI) | GPI-9 Situational awareness GPI-17 Implementation of data link applications GPI-18 Electronic information services | 
Main Dependencies | (excerpt from dependency diagram to be included in V3). Predecessor of: B1-40 (but can also be combined with it) | 
Global Readiness Checklist |  | Status
 | Standards Readiness | Ready
 | Avionics Availability | Ready
 | Ground Systems Availability | Ready
 | Procedures Available | Ready
 | Operations Approvals | Ready

## Slide 3: Module N° B0-40 - Baseline
Prior to this module, air-ground communications used voice radio (VHF or HF depending on the airspace)
  Known limitations in quality, bandwidth and security and areas with no radar surveillance.
High density airspace controllers spend 50% of their time talking to pilots on the VHF voice channels where frequencies are a scarce resource
  This represents a significant workload for controllers and pilots

## Slide 4: Module N° B0-40 – Change Brought by the Module
Element 1  ADS-C over Oceanic and Remote Areas
  ADS-C provides an automatic dependent surveillance service over oceanic and remote areas, through the exploitation of position messages sent automatically by aircraft over data link at specified time intervals (ADS-Contract).
Element 2  Continental CPDLC
  The applications allow pilots and controllers to exchange messages with a better quality of transmission.

## Slide 5: Module N° B0-40 –Intended Performance Operational Improvement
Capacity | Reduced separations allow increasing the offered capacity.
Efficiency | Routes/tracks and flights can be separated by reduced minima, allowing to apply flexible routings and vertical profiles closer to the user-preferred ones.
Flexibility | permits to make route changes easier
Safety | Increased situational awareness; better support to SAR
CBA | The business case has proven to be positive
Capacity | Reduced communication workload & better organisation of controller tasks allow to increase sector capacity
Safety | Increased situational awareness; reduced occurrences of misunderstandings; solution to stuck mike situations
CBA | The European business case has proven to be positive due.
Element 1
ADS-C over Oceanic and Remote Areas
Element 2
Continental CPDLC

## Slide 6: Module N° B0-40 – Necessary Procedures (Air & Ground)
Procedures have been described and are available in ICAO documents: Manual of Air Traffic Services Data Link Applications (Doc 9694), GOLD Global Operational Data Link Document

## Slide 7: Module N° B0-40 – Necessary System Capability
Avionics
  Data Link implementations are based on two sets of ATS Data link services: FANS 1/A and ATN B1, both will exist. FANS1/A is deployed in Oceanic and Remote regions whilst ATN B1 is being implemented in Europe
  Dual stack implementation (FANS 1/A and ATN B1) in the aircraft
Ground Systems
  ADS-C process and display position messages.
  CPDLC messages need to be displayed to the relevant ATC unit.

## Slide 8: Module N° B0-40 – Training and Qualification Requirements
Automation support is needed for both the pilot and the controller which therefore will have to be trained to the new environment and to identify the aircraft/facilities which can accommodate the data link services in mixed mode environments.
Training in the operational standards and procedures are required for this module
Likewise, the qualifications requirements are identified in the regulatory requirements

## Slide 9: Module N° B0-40 –Regulatory/Standardization needs and Approval Plan (Air & Ground)
Regulatory/Standardization:
  Use current published requirements .
  New ICAO OPLINK Ops Guidance is under development
Approval Plans:
  Must be in accordance with application requirements

## Slide 10: Module N° B0-40 – Reference Documents (1/2)
Standards
  Commission Regulation (EC) No 29/2009 of 16 January 2009 laying down requirements on data link services for the single European sky
  EUROCAE ED-100A / RTCA DO-258A, Interoperability Requirements for ATS Applications using ARINC 622 Data Communications
  EUROCAE ED-110 / RTCA DO-280, Interoperability Requirements Standard for Aeronautical Telecommunication Network Baseline 1 (Interop ATN B1)
  EUROCAE ED-120 / RTCA DO-290, Safety and Performance Requirements Standard For Initial Air Traffic Data Link Services In Continental Airspace (SPR IC)
  EUROCAE ED-122 / RTCA DO-306, Safety and Performance Standard for Air Traffic Data Link Services in Oceanic and Remote Airspace (Oceanic SPR Standard)
  EUROCAE ED-154 / RTCA DO-305, Future Air Navigation System 1/A – Aeronautical Telecommunication Network Interoperability Standard (FANS 1/A – ATN B1 Interop Standard)
Procedures: Nil

## Slide 11: Module N° B0-40 – Reference Documents (2/2)
Guidance Material
  ICAO Doc 9694, Manual of Air Traffic Services Data Link Applications;
  New OPLINK Ops Guidance (under development).
Approval Documents
  ICAO Doc 9694, Manual of Air Traffic Services Data Link Applications;
  FAA AC20-140A, Guidelines for Design Approval of Aircraft Data Link Communication Systems Supporting Air Traffic Services (ATS);
  RTCA/EUROCAE DO-306/ED-122;
  RTCA/EUROCAE DO-305/ED-154;
  RTCA/EUROCAE DO-290/ED-120;
  RTCA/EUROCAE DO-280/ED-110B;
  RTCA/EUROCAE DO-258A/ED-100A;
  EC Regulation No. 29/2009: Datalink Services Implementing Rule;
  New OPLINK Material under development.

## Slide 12: Module N° B0-40 Implementation - Benefits and Elements
Improved Safety and Efficiency through the initial application of Data Link En-Route
Benefits - Main Key Performance Areas (KPA) |  |  |  |  | 
KPAs | Access | Capacity | Efficiency | Environment | Safety
Applicable | N | Y | Y | N | Y
Elements:
  -ADS-C over oceanic and remote areas using FANS1/A or ATN B1
  -VDL Mode 2 /Continental CPDLC
  To be reflected in ANRF